## Slide 1: BASICS OF LINKED (BUILDING) DATA
Jeroen Werbrouck
June 10th, 2024
4th Summer School of Linked Data in Architecture and Construction
@Ruhr Universität Bochum,

## Slide 2: Who am I?
Master of Engineering: Architecture – (UGent, 2013-2018)
Phd Research - (UGent/RWTH Aachen, 2019-2024)
  H2020 BIM4Ren
  Teaching assistant UGent
  FWO grant “strategic basic research”

## Slide 3: Presentation outline
The Digital Built Environment
The Evolution of the Web
Knowledge Graphs
Linked Building Data

## Slide 4: THE DIGITAL BUILT ENVIRONMENT

## Slide 5: The digital built environment
Painting: In Praise of Dialectics (1936) R. Magritte

## Slide 6
HVAC ENGINEER
ARCHITECT
It’s a ventilation opening
it allows natural light to flood into the space
ENERGY CONSULTANT
it’s a part of the building
envelope with poor insulation
STRUCTURAL ENGINEER
The load of the mass above the window must be redirected
The AEC Industries: Architecture, Engineering and Construction
Painting: In Praise of Dialectics (1936) R. Magritte
© icons by Vitaly Gorbachev

## Slide 7
HVAC ENGINEER
ARCHITECT
It’s a ventilation opening
it allows natural light to flood into the space
ENERGY CONSULTANT
it’s a part of the building
envelope with poor insulation
STRUCTURAL ENGINEER
The load of the mass above the window must be redirected
The AEC Industries: Architecture, Engineering and Construction
Painting: In Praise of Dialectics (1936) R. Magritte
© icons by Vitaly Gorbachev
BIM?
BIM is the creation and use of coordinated, consistent, and computable information about a building project in design, in construction and in building operation and management.
BIM provides a digital representation of the physical and functional characteristics of a facility.

## Slide 8
HVAC ENGINEER
ARCHITECT
It’s a ventilation opening
it allows natural light to flood into the space
ENERGY CONSULTANT
it’s a part of the building
envelope with poor insulation
STRUCTURAL ENGINEER
The load of the mass above the window must be redirected
The AEC Industries: Architecture, Engineering and Construction
Painting: In Praise of Dialectics (1936) R. Magritte
© icons by Vitaly Gorbachev
BIM?
A basic premise of BIM is collaboration
      by different stakeholders
      at different phases of the life cycle of a facility
      to insert, extract, update or modify information in the BIM
      to support and reflect the roles of that stakeholder.
INTEROPERABILITY? = Need for standardisation!

## Slide 9: Collaboration in AEC: CDEs
CDE
Building Information Model (“BIM”)

## Slide 10: Standardisation in AEC
Industry Foundation Classes (IFC)
BIM Collaboration Format (BCF)
green building XML (gbXML)
…

## Slide 11: Industry Foundation Classes
Terminology & structure
The actual data

## Slide 12: IFC Technical Roadmap – move to the web
https://www.buildingsmart.org/about/technical-roadmap/

## Slide 13
HVAC ENGINEER
ARCHITECT
It’s a ventilation opening
it allows natural light to flood into the space
ENERGY CONSULTANT
it’s a part of the building
envelope with poor insulation
STRUCTURAL ENGINEER
The load of the mass above the window must be redirected
The AEC Industries: Architecture, Engineering and Construction
Painting: In Praise of Dialectics (1936) R. Magritte
© icons by Vitaly Gorbachev

## Slide 14
HVAC ENGINEER
ARCHITECT
It’s a ventilation opening
it allows natural light to flood into the space
ENERGY CONSULTANT
it’s a part of the building
envelope with poor insulation
STRUCTURAL ENGINEER
The load of the mass above the window must be redirected
FACILITY MANAGER
it’s an asset that requires cleaning and painting
The AECO Industries: Architecture, Engineering, Construction and Operations
Painting: In Praise of Dialectics (1936) R. Magritte
© icons by Vitaly Gorbachev

## Slide 15
HVAC ENGINEER
ARCHITECT
It’s a ventilation opening
it allows natural light to flood into the space
ENERGY CONSULTANT
it’s a part of the building
envelope with poor insulation
STRUCTURAL ENGINEER
The load of the mass above the window must be redirected
FIRE SAFETY ENGINEER
it’s a fire escape
ACOUSTIC CONSULTANT
it’s a surface with low
sound absorption!!!
PAINTER
It’s just a painting
OWNER
MY curtains must close automatically when it’s dark
FACILITY MANAGER
it’s an asset that requires cleaning and painting
Painting: In Praise of Dialectics (1936) R. Magritte
© icons by Vitaly Gorbachev

## Slide 16
Painting: In Praise of Dialectics (1936) R. Magritte
© icons by Vitaly Gorbachev

## Slide 17
SOIL MAPS API
this is a site with geothermY potential
GOVERNMENT API
Does this building comply
to accessibility rules?
There’s a storm today. Don’t go to the building site.
This is an archaeologically interesting location.
we MUST DIG OUT the dino’s BEFORE STARTING THE WORK!
INFRASTRUCTURE API
The nearest railway station
is 3km away.
WEATHER API
ARCAHEOLOGY API
The AECOOHHGGQSDFXYZ🍕 Industry?
Painting: In Praise of Dialectics (1936) R. Magritte
© icons by Vitaly Gorbachev

## Slide 18: The AECO(OHHGGQSDFXYZ🍕) Industry?
Ever-increasing need for domain-independent information reuse
  Architecture
  Engineering
  Construction
  Operations
  Owner
  History & Heritage
  Geospatial
  Government
  User Preferences
  …

## Slide 19
SOIL MAPS API
this is a site with geothermY potential
GOVERNMENT API
Does this building comply
to accessibility rules?
There’s a storm today. Don’t go to the building site.
This is an archaeologically interesting location.
we MUST DIG OUT the dino’s BEFORE STARTING THE WORK!
INFRASTRUCTURE API
The nearest railway station
is 3km away.
WEATHER API
ARCAHEOLOGY API
ONE SINGLE, CENTRALISED PLATFORM?
Painting: In Praise of Dialectics (1936) R. Magritte
© icons by Vitaly Gorbachev

## Slide 20: Data Federation
Every building is the sum of the
(domain-specific) contributions
of multiple stakeholders
Direct stakeholders: architect, engineer, owner, …
Indirect stakeholders: government, infrastructure, …
LEGENDA

## Slide 21: Data Federation
Every stakeholder
takes part in multiple projects
LEGENDA

## Slide 22: Web-based Building Data

## Slide 23: THE EVOLUTION OF THE WEB

## Slide 24: The World Wide Web
Distributed by design
Decentralized
For everyone
Graph of links between things
Dynamic
Open and closed

## Slide 25
Read-only
Web of documents
Web 1.0

## Slide 26
Read-write-publish
Web of people
Web 2.0

## Slide 27
Read-write-execute
Web 3.0

## Slide 28: Information on the Web
People can parse the web of documents and extract information from them to come to insights.
We need to help machines to understand the web, so machines can help us understand things.
If machines have access to the data about things, they can do a better job while processing documents.

## Slide 29: Web services: Fetching Data (GET)
REST API
1. Show me this webpage
4. there you go
3. Build webpage with
most recent content
2a. Retrieve 5 most recent wall posts
2b. store image

## Slide 30: Web services: Posting Data (POST)
REST API
1. Create this new wall post
3. Done!
2. Store text, title, etc.
2b. Retrieve associated images

## Slide 31: Content Negotiation
Retrieve 5 most recent wall posts
Retrieve associated images
REST API
REST API
there you go
Person X requested wall posts
Give me the wall posts in JSON

## Slide 32: Web of documents

## Slide 33: Web of Data

## Slide 34: The Semantic Web is needed: a Web of Data
“The Semantic Web is an extension of the current web in which information is given well-defined meaning, better enabling computers and people to work in cooperation.” [Tim Berners-Lee et al. 2001.]
Specific goals:
      Build a description language with standard semantics
      Make semantics machine-processable and understandable
      Incorporate logical infrastructure to reason about resources
      W3C Specificaions: Resource Description Framework (RDF) and SPARQL

## Slide 35: KNOWLEDGE GRAPHS

## Slide 36: Graph Theory and Graph Thinking
Graphs as mathematical structures used to model pairwise relations between objects
Graph theory was pioneered by Euler in the 18th century, and has been actively researched and improved by mathematicians, sociologists, anthropologists, etc.
only in the past few years have graph theory and graph thinking been applied to information management
Possible to leverage complex and dynamic relationships in highly connected data

## Slide 37: What is a Ggraph?
vertices / nodes and edges / relationships
General-purpose, expressive structure allows us to model all kinds of scenarios
Focus on the connections and links: a lot more than in relational databases

## Slide 38: Graph Data Example: a social network
Any social network’s data is easily represented as a graph
Each node is labeled User, indicating its role in the network. These nodes are then connected with relationships, which help further establish the semantic context: who follows who?

## Slide 40: Knowledge Graphs
https://aws.amazon.com/neptune/

## Slide 41: Knowledge Graphs
https://aws.amazon.com/neptune/

## Slide 42: A knowledge graph
https://aws.amazon.com/neptune/

## Slide 43: Federated Knowledge Graphs
https://aws.amazon.com/neptune/

## Slide 44: linked open data

## Slide 46: Linked Open Data Cloud
https://lod-cloud.net/

## Slide 47: Knowledge Graphs: RDF
GIVES
PRESENTATION
JEROEN
LIVES IN
GHENT
JEROEN
TAKES PLACE IN
BOCHUM
PRESENTATION
“Triples” are basic sentences of the form “subject – predicate – object”
Everything you can talk about is a “resource”
predicate
object
subject
IS A
CITY
GHENT
IS A
CITY
BOCHUM

## Slide 48: Knowledge Graphs: RDF
Multiple (overlapping) triples form a “directed graph”
GIVES
PRESENTATION1
JEROEN
LIVES IN
GHENT
IS A
CITY
TAKES PLACE IN
BOCHUM
IS A
Instance
Class

## Slide 49: Knowledge Graphs: RDF
Uniform Resource Identifiers (URIs)
Literals
GIVES
https://jeroen.werbrouck.me/presentations/LDACpresentation
http://purl.org/oslo/ns/localgov#residence
https://dbpedia.org/page/ghent
http://www.w3.org/1999/02/22-rdf-syntax-ns#type
https://dbpedia.org/page/City
https://dbpedia.org/page/Presentation
https://jeroen.werbrouck.me/profile/card#me
“LDAC_introduction.pptx”
http://purl.org/dc/terms/title
http://www.w3.org/1999/02/22-rdf-syntax-ns#type
Literal
URI

## Slide 50: Knowledge Graphs: RDF
Uniform Resource Identifiers (URIs)
swpo:givesPresentations
https://jeroen.werbrouck.me/presentations/LDACpresentation
oslo:residence
https://dbpedia.org/page/Ghent
rdf:type
https://dbpedia.org/page/City
https://dbpedia.org/page/Presentation
https://jeroen.werbrouck.me/profile/card#me
“LDAC_introduction.pptx”
dct:title
rdf:type
PREFIXES:
@prefix rdf: <http://www.w3.org/1999/02/22-rdf-syntax-ns#>
@prefix dct: <http://purl.org/dc/terms/>
@prefix oslo: <http://purl.org/oslo/ns/localgov#>
@prefix schema: <http://schema.org/>
@prefix swpo: <http://sw-portal.deri.org/ontologies/swportal#>
(alternative: “a” )
schema:location

## Slide 51: Knowledge Graphs: RDF
Uniform Resource Locators (URLs)
swpo:givesPresentations
https://jeroen.werbrouck.me/presentations/phdpresentation
oslo:residence
https://dbpedia.org/page/Ghent
https://dbpedia.org/page/City
https://dbpedia.org/page/Presentation
https://jeroen.werbrouck.me/profile/card#me
“The Web as a Common …”
:me a foaf:Person ;
foaf:firstName “Jeroen” ;
foaf:lastName “Werbrouck” .
…
rdf:type
dct:title
rdf:type
schema:location
leads to

## Slide 52: Notation: Turtle (.ttl)
Machine- and human-readable syntax
Prefixes / Namespaces
Punctuation
  . ends a triple
  ; triple has the same subject
  , triple has the same subject / predicate
Full URLs are wrapped: <url>
@prefix bot: <https://w3id.org/bot#> .
@prefix : <http://mydata.org/project1#> .
:wall1 a bot:Element ,
beo:Wall .
:space1 a bot:Space ;
bot:adjacentElement :wall1 .

## Slide 53: Querying: SPARQL
SPARQL Protocol And RDF Query Language
Very expressive
SELECT (output = table)
CONSTRUCT (output = RDF graph)
ASK (output = Boolean)
PREFIX bot: bot: <https://w3id.org/bot#>
SELECT ?sp ?w WHERE {
?sp a bot:Space ;
bot:adjacentElement ?w .
}

## Slide 54
INTERACTIVE: make a graph about yourself with some
instances (e.g. you, friends, family, …)
relationships (e.g. “hasFriend”, “hasHobby”, “hasAge”, …)
classes (e.g. “Friend”, “Hobby”)
Literals (e.g. a number (age), a string (name), …)
! You can use example URI’s as prefixes
(they don’t need to resolve to an actual Web-address to be correct syntax)
Playground: https://madsholten.github.io/sparql-visualizer/

## Slide 55: Linked Building Data

## Slide 56: Knowledge graphs in AECO
Image source: © Mads Holten Rasmussen, bSI London 2017

## Slide 57: ifcOWL
Certified standard, RDF equivalent IFC-SPF
Pauwels, P., & Terkaj, W. (2016). EXPRESS to OWL for construction industry: Towards a recommendable and usable ifcOWL ontology. Automation in construction, 63, 100-133.
http://www.buildingsmart-tech.org/ifcOWL/IFC4_ADD2#

## Slide 58: Building Topology Ontology
https://w3id.org/bot#

## Slide 59: BuildingElement Ontology: product taxonomy
http://pi.pauwel.be/voc/buildingelement#
http://pi.pauwel.be/voc/distributionelement#

## Slide 60: Semantic graph with sensors and building topology

## Slide 61: Reference ontologies
BOT https://w3id.org/bot#
BEO https://pi.pauwel.be/voc/buildingelement/
MEP https://pi.pauwel.be/voc/distributionelement/
OMG https://w3id.org/omg#
FOG https://w3id.org/fog#
BPO https://www.w3id.org/bpo#
OPM https://www.w3id.org/opm#
Revit to LBD exporter: on demand
IFC to LBD converter: on demand

## Slide 63: “Hybrid” Knowledge graphs
Heterogeneity! (“Does everything need to be RDF now?”)
How can we link geometry, images, point clouds…?
  Direct linking
  Multi-models in AEC
    ICDD (ISO 21597)
inst:space1 bot:hasSimple3DModel
“v 0 0 0
v 0 6500 0
v 0 6500 2750
n 0 0 1
f 1//1 2//1 3//1”

## Slide 64: “Hybrid” Knowledge graphs
Heterogeneity! (“Does everything need to be RDF now?”)
How can we link geometry, images, point clouds…?
  Direct linking
  Multi-models in AEC
    ICDD (ISO 21597)
inst:space1 bot:has3DModel <http://example.org/model1.gltf> .

## Slide 65: Multi-models: ICDD
(ZIP) CONTAINER
(ISO 21597 – ICDD)
LINKSET
Heterogeneous containers
index.rdf describes the resources/documents
links.rdf describes the relationships between sub-document identifiers

## Slide 66: THANK YOU!
Jeroen Werbrouck
Ghent University
RWTH Aachen University
jeroen.werbrouck@ugent.be